## Slide 1: Root Cause Analysis - Response Joint Legislative Oversight Hearing What Caused the Southern California Gas Company’s 2015 Blowout at Aliso Canyon? A Closer Look at the History of the Field and the Emergency Response
Briana Mordick, Senior Scientist, Natural Resources Defense Council
6 August 2019

## Slide 2
Root Cause | Solution | Addressed by Regulation? | DOGGR Rule
No corrosion protection No cement outside of 7 in. casing Bacteria in the “B” annulus water External corrosion initiated on the 7 in. casing External corrosion on 7 in. casing had removed 85% of wall 7 in. casing corrosion grew over time | Cement production casing to surface | Not Required | 1726.5(b)(7)(B) Intermediate and production casings, if not cemented to the surface, are cemented in accordance with the requirements of Section 1722.4.
ACTION NEEDED Address through current DOGGR well construction rulemaking process |  |  | 
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.

## Slide 3
Root Cause | Solution | Addressed by Regulation? | DOGGR Rule
No regulations on production casing wall thickness inspection No down hole inspection log run on SS-25 7 in. casing corrosion not detected External corrosion on 7 in. casing had removed 85% of wall 7 in. casing corrosion grew over time | Regulations should require wall thickness inspection | Yes (Included in the latest regulations) | 1726.6(a)(2) Casing wall thickness inspection at least once every 24 months Compare results to determine corrosion rate Remediate if cannot contain 115% of maximum operating pressure Less frequent inspection schedule may be approved.
ACTION NEEDED If casing inspection reveals potential for significant corrosion, require development of corrosion monitoring program based on risk management plan Eliminate variance for casing inspection frequency |  |  | 
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.

## Slide 4
Root Cause | Solution | Addressed by Regulation? | DOGGR Rule
TIMP used, but no SIMP Not proactive in managing failures No well integrity management in place No proactive focus on well integrity Reacted and mitigated casing leaks Focus on reservoir and facilities Complacency regarding well blowout control SS-25 ranked low for production casing inspection Only acted on high priority wells Probability of the shallow casing rupture not understood Did not execute on 1988 memo for 22-25 No Risk Assessment | Implement a Risk Based Integrity Management Plan | Yes (Included in the latest regulations) | 1726.3. Risk Management Plans.
ACTION NEEDED Public notice and comment process Detailed guidance for granting variances |  |  | 
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.

## Slide 5
Root Cause | Solution | Addressed by Regulation? | DOGGR Rule
SCG did not realize that this was exposed to corrosive environment Reacted and mitigated casing leaks Probability of the shallow casing rupture not understood | Conduct casing corrosion study | Yes | 1726.3(d)(4) Corrosion monitoring, evaluation, and mitigation including consideration of at least the following: Evaluation of tubular integrity and identification of defects caused by corrosion or other chemical or mechanical damage; Corrosion potential of wellbore produced fluids and solids, including the impact of operating pressures, temperatures, and compositions on the corrosion potential of wellbore fluids and analysis of partial pressures; Corrosion potential of annular and packer fluid; Corrosion potential of current flows associated with cathodic protection systems; Corrosion potential of all formation fluids, including fluids in formations above the storage zone; and Corrosion potential of uncemented casing.
ACTION NEEDED Public notice and comment process Guidance |  |  | 
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.

## Slide 6
Root Cause | Solution | Addressed by Regulation? | DOGGR Rule
Failure analysis was not considered necessary Reacted and mitigated casing leaks No failure analysis of any of the prior casing failures Not proactive in managing failures Probability of the shallow casing rupture not understood | Conduct casing failure analysis | Not Specifically (would be expected to be part of a risk management plan) | 1726.3. Risk Management Plans.
ACTION NEEDED Address through current DOGGR well construction rulemaking process Public notice and comment Guidance |  |  | 
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.

## Slide 7
Root Cause | Solution | Addressed by Regulation? | DOGGR Rule
Complacency regarding well blowout control Did not use available data They did not analyze the flow test data Fluid had high TCT No evidence of kill modeling Underestimated the well flow rate for kill attempts Unsuccessful top kill attempts No lessons learned from prior kill attempt was implemented Kill attempt #1 failed October 24, 2015 Kill attempts #2-6 failed (November 12-25) Routine kill operations adequate for previous casing leaks Previous unsuccessful kill attempts Thought they could top kill Insufficient pump rates and fluid density Modeling was done with the 25MMscf/D Took decision to drill the relief well on November 20, 2015 Times to drill a directional well to 8650 feet and intersect No adequate Emergency Response Plan exists | Well-specific detailed well-control plan | Yes | 1726.3.1 Emergency Response Plan
ACTION NEEDED Explicitly require well-specific plans Public notice and comment Guidance |  |  | 
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.

## Slide 8
Root Cause | Solution | Addressed by Regulation? | DOGGR Rule
Downhole annulus safety system not required by regulations 7 in. production casing acted as the single barrier No downhole annulus safety system to control the well SCG using injection/withdrawal primarily through casing | Tuber packer completion-dual barrier system | Yes (included in the latest regulations) | 1726.5(b)(1) The well has been constructed with both primary and secondary mechanical well barriers to isolate the storage gas within the storage reservoir and transfer storage gas from the surface into and out of the storage reservoir.
ACTION NEEDED Explicitly require injection and withdrawal to occur only through tubing set on a packer |  |  | 
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.

## Slide 9
Root Cause | Solution | Addressed by Regulation? | DOGGR Rule
Downhole annulus safety system not required by regulations 7 in. production casing acted as the single barrier No downhole annulus safety system to control the well SCG using injection/withdrawal primarily through casing | Tuber packer completion-dual barrier system | Yes (included in the latest regulations) | 1726.5(b)(1) The well has been constructed with both primary and secondary mechanical well barriers to isolate the storage gas within the storage reservoir and transfer storage gas from the surface into and out of the storage reservoir.
ACTION NEEDED Explicitly require injection and withdrawal to occur only through tubing set on a packer |  |  | 
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.

## Slide 10
Company Name | Field Name | Reservoir Name | Field Type | County | Working Gas Capacity (mcf) | Total Field Capacity (mcf) | Maximum Daily Delivery (mcf) | Reservoir Discovery Date | Field Discovery Date
WILD GOOSE STORAGE INC | WILD GOOSE | L4 | Depleted Field | Butte | 75,000,000 | 86,000,000 | 950,000 | 1951 | 1951
CENTRAL VALLEY GAS STORAGE LLC | PRINCETON GAS | PRINCETON GAS | Depleted Field | Colusa | 11,000,000 | 12,400,000 | 300,000 | 1953 | 1953
PACIFIC GAS AND ELECTRIC COMPANY | PLEASANT CREEK | PETERS | Depleted Field | Yolo | 2,250,000 | 7,328,500 | 70,000 | 1948 | 1948
LODI GAS STORAGE LLC | KIRBY HILLS | WAGENET | Aquifer | Solano | 10,000,000 | 12,000,000 | 200,000 | N/A | N/A
LODI GAS STORAGE LLC | KIRBY HILLS | DOMENGINE | Depleted Field | Solano | 5,000,000 | 7,000,000 | 50,000 | 1945 | 1945
PACIFIC GAS AND ELECTRIC COMPANY | LOS MEDANOS | DOMENGINE | Depleted Field | Contra Costa | 17,946,000 | 29,139,000 | 400,000 | 1958 | 1958
PACIFIC GAS AND ELECTRIC COMPANY | MCDONALD ISLAND | MCDONALD | Depleted Field | San Joaquin | 82,000,000 | 136,568,000 | 1,680,000 | 1936 | 1936
LODI GAS STORAGE LLC | LODI | DOMENGINE | Depleted Field | San Joaquin | 8,500,000 | 10,500,000 | 250,000 | 1943 | 1943
LODI GAS STORAGE LLC | LODI | MIDLAND | Depleted Field | San Joaquin | 8,500,000 | 10,500,000 | 250,000 | 1953 | 1943
GILL RANCH STORAGE LLC | GILL RANCH | STARKEY | Depleted Field | Madera | 20,000,000 | 23,500,000 | 650,000 | 1956 | 1943
SOUTHERN CALIFORNIA GAS COMPANY | LA GOLETA | VAQUEROS | Depleted Field | Santa Barbara | 21,500,000 | 46,089,073 | 420,000 | 1932 | 1932
SOUTHERN CALIFORNIA GAS COMPANY | ALISO CANYON | SESNONFREW | Depleted Field | Los Angeles | 86,000,000 | 167,525,000 | 1,860,000 | 1940 | 1938
SOUTHERN CALIFORNIA GAS COMPANY | HONOR RANCHO | WAYSIDE 13 | Depleted Field | Los Angeles | 24,200,000 | 44,300,000 | 1,000,000 | 1950 | 1950
SOUTHERN CALIFORNIA GAS COMPANY | PLAYA DEL REY | PUENTE | Depleted Field | Los Angeles | 2,400,000 | 6,861,545 | 480,000 | 1929 | 1929
Notes: 1722.4 Intermediate and production casings, if not cemented to the surface, shall be cemented with sufficient cement to fill the annular space to at least 500 feet above oil and gas zones, and anomalous pressure intervals. Sufficient cement shall also be used to fill the annular space to at least 100 feet above the base of the freshwater zone, either by lifting cement around the casing shoe or cementing through perforations or a cementing device placed at or below the base of the freshwater zone.