## Slide 1: SS-25 Root Cause Analysis
California Joint Legislative Oversight Hearing
August 6, 2019

## Slide 2: ACKNOWLEDGEMENTS
CPUC
DOGGR
SOCALGAS
Service Companies

## Slide 3: Phases
Root cause:
  Systematic process for identifying the root causes of problems or events and determining methods for responding to and preventing them
Phase 0: Data collection, collation and analyses
Phase 1: Site Evidence collection and documentation
Phase 2: Site restoration to rig readiness
Phase 3: Tubing, casing, and wellhead extraction
Phase 4: Non-destructive evaluation and metallurgical examination
Phase 5: Integration, interpretation, and final report

## Slide 4: SS-25 Wellbore for Gas Storage
Injection and withdrawal through the tubing and casing
Casing flow was through open ports in the annular flow safety system above the packer
11 ¾ in. cementing problems
No leaks or failures in SS-25 until October 23, 2015

## Slide 5: SS-25 Failure
SS-25 Root Cause Analysis

## Slide 7: 7 in. Casing Failure Sequence
External corrosion with 85% wall reduction
Corrosion caused by microbes resulting in grooves
Notch acted like a stress concentrator
Large patch of corrosion
Axial rupture
Cooled (-76oF to -38oF) and then circumferential parting
Two separate events-failure sequence

## Slide 8: 7 in. Corrosion
Annulus groundwater ingress and egress
Dry and wet seasons
External corrosion due to microbes

## Slide 9: 7 in. Casing Failure Timeline on Oct. 23
October 23, 2015
  Well opened for injection between 3 and 4 AM
  Axial rupture happened first
  Gas flow increased to a total of 160 mmscf/D
  Metal cooling resulted in brittleness and circumferential parting within hours of axial rupture
  All failures same day

## Slide 10: Post Leak Events
SS-25 Root Cause Analysis

## Slide 11: Flow Rate / Kill Modeling
Chart: Gas Rate (MMscf/D)
Kill 1 | 0 | 1000
Kill 2 | 0 | 1000
Kill 3 | 0 | 1000
Kill 4 | 0 | 1000
Kill 5 | 0 | 1000
Kill 6 | 0 | 1000
Kill 7 | 0 | 1000
Modeling and Assessment predicts that kill could have been successful with heaver fluids at a higher pump rate

## Slide 12: Aliso Canyon Casing Integrity
SS-25 Root Cause Analysis

## Slide 13: Aliso Canyon Casing Integrity
Historical Casing Failures
  Mitigated immediately
  No failure analyses or further investigation
1988 Memo on Casing Inspection
  7 out of 20 logged (5 had external corrosion)
GRC 2016-Testimony in 2014
  Risk Assessment as part of SIMP
Chart: Number of Aliso Canyon Gas Storage Wells Reviewed, Wells with Casing Problems and Casing Failures by Spud Date
| 1939-49 | 1950-59 | 1960-69 | 1970-79 | 1980-89 | 1990-99 | 2000-09 | 2010-15
No. Wells Reviewed (124) | 38 | 22 | 1 | 33 | 8 | 9 | 8 | 5
No. Wells with Prob. (49) | 15 | 9 | 1 | 18 | 5 | 1
No. Casing Prob. (99) | 35 | 10 | 2 | 39 | 12 | 1
Pre-2015 Approach more Reactive rather than Proactive

## Slide 14: Root Cause Analysis
SS-25 Root Cause Analysis

## Slide 15: Causes
Direct
  Axial rupture due to microbial corrosion on the OD of the 7 in. casing
  Unsuccessful top kills because of insufficient fluid density and pump rates
Root Causes Identified

## Slide 16: Root Cause Solutions
The RCA identified solutions that would have prevented the primary effect
Nearly all have been implemented to meet SoCalGas current practices and DOGGR regulations updated after 2015
Solutions:
  Risk based well integrity management system
  Casing wall thickness inspections
  Tubing-packer completions – dual barrier system
  Real-time well surveillance of surface pressures (tubing and annuli)
  Detailed well-specific well control plans
  Casing corrosion study
Additional proposed solutions:
  Conduct casing failure analyses
  Cement surface and production casings to surface for new wells
  Implement cathodic protection when appropriate

## Slide 17: Phase 5: Integration, Interpretation, and Final Report
Main report released May 16, 2019
27 Supplementary reports released May 31, 2019
Report links on CPUC website

## Slide 18: Questions?
SS-25 Root Cause Analysis